Project Thistle Specification

- RISC architecture, load/store
- 8-bit System on solder-less breadboard
- Uses 74LS TTL series or compatible logic
- Variable clock speed: 0.1Hz → 10Hz, either astable or monostable
- 256 Bytes of RAM – Hand programmable
- 2 general purpose 8-bit registers and one 8-bit null register
- An I/O register connected to 4 seven segment displays and a DIP switch, supports 2's complement
- An 8-bit ALU, supports 2's complement

Instruction Set:

- LD : 0000 + xxReg + Address	Registers: A → 00
- ST : 0001 + xxReg + Address B → 01
- ADD : 0010 + xxxx IO → 10
- SUB : 0011 + xxxx NR → 11
- MOV : 0100 + R1R2
- IN : 0101 + xxReg
- CLR : 0110 + xxReg
- HLT : 0111 + xxxx
- JC : 1000 + xxxx + Address
- JNC : 1001 + xxxx + Address
- JMP : 1010 + xxxx + Address
- JR : 1011 + xxReg
- TWC : 1100 + xxxx
- NOP : 1101 + xxxx

Syntax:

Registers: A,B,NR,IO
Addresses: 0 → 255

- LD Reg, Addr. → Stores value from address into selected register
- ST Reg, Addr. → Stores value from selected register into address
- ADD → Adds contents of A and B, puts result in A
- SUB → Subs B from A, puts result in A
- MOV Reg1,Reg2 → Moves contents of register 1 to register 2
- IN Reg → Halts system until user writes to I/O register
- CLR Reg → Clears selected register
- HLT → Halts system
- JC Addr. → Jumps to address if the carry bit is set
- JNC Addr. → Jumps to address if the carry bit is not set
- JMP Addr. → Jumps to address
- JR Reg → Jumps to address in selected register
- TWC → Toggles the 2's complement of the output display, default binary
- NOP →Null operation

Block Diagram: